CRATE/PALLET LUMBER CHARTS

HOW TO READ THE CRATE LUMBER CHART

The first column of the chart is the crate number, which is also the crate size.  For example 3825, the first two numbers 38 _ _ refer to the crate length 38”.  The third number _ _ 2 _ refers to the height of the crate (2 board high).  The last number _ _ _ 5 refers to the width of the crate which in this example is 5 boards wide.

Note:  Boards wide or high refer to 1” x 6” boards.

If the crate number is followed by an “A”, this means that the crate is built with four (4) legs instead of the normal three (3).

Note:  The “A” crates may be built with or without “dummy boards” at the request of the requester.  “Dummy boards” are 2” x 4” crosspieces which are placed length wise between the outside two legs on one side of the crate (2 per crate).  This is to prevent the forklift from picking up the crate from the one side.

Read across chart to find the size and quantity of lumber required for each crate.

HOW TO READ THE PALLET LUMBER CHART

In the first column on the pallet lumber chart are the pallet numbers.  This number refers to the size of the pallet in inches in length and width.  The first two numbers the length of the pallet and the last two numbers are the width of the pallet.  For example 2638P is 26” long by 38” wide.  “P” refers to pallet.

If the P of the pallet number is followed by a number 1 or 2, this refers to a two (2) part pallet and equal amounts of both are required.

Read across the pallet chart to find the description of the pallet, lumber size and quantity required for each pallet.

CRATE LUMBER CUTTING TOLERANCES

All lumber cuts should be as close to the specification as possible.  Due to the fact that the “Bundle Chain Saw” does not always cut 100% accurate there is an allowable tolerance for each cut as stated below.

1.	1" x 6" Tops and Bottoms - Should be as close to specs as possible, but can still be used up to 1/2" longer or shorter.

2.	1" x 6" sides - Can be no longer than specs, but can be up to 1/2" shorter.

3.	1" x 6" ends - Should be as close to specs as possible, but may be up to 1/4" longer or shorter.

4.	2" x 4" sides (outside) - Should be as close to specs as possible, but may be up to 1/2" longer or shorter.

5.	2" x 4" sides (inside) - Should be as close to specs as possible, but can be NO longer and up to 1/2" shorter.

6.	2" x 4" tops - Should be as close to specs as possible, but can be NO longer and up to 1/2" shorter.

7.	2" x 4" bottoms - Should be s close to specs as possible, but can be NO longer and up to 1/2" shorter.

2" x 4" crosspiece (for A crate) - Should be as close to specs as possible, but can be NO longer and up to 1/2" shorter.

| Lumber size/crate part/crate size | 1 X 6 Tops & Bottoms | # of pcs per crate |
| --- | --- | --- |

1 X 6

| Sides | No. of pieces per crate |
| --- | --- |

1 X 6

| Ends | No. of pieces per crate |
| --- | --- |

2 X 4

| Outside Sides | No. of pieces per crate |
| --- | --- |

2 X 4

Inside Sides

No. of

pieces per crate

2 X 4

| Top | No. of pieces per crate |
| --- | --- |

2 X 4

| Bottoms | No. of pieces per crate |
| --- | --- |

2 X 4

| Bottom Cross Piece | No. of ps per crate |
| --- | --- |
| 1822 | 18 ft. | 4 | 18 ft. | 4 | 17.5” | 4 | 11.25” | 18 | N/A | N/A | 17.5” | 9 | 17.5” | 9 | N/A | N/A |
| 2935 | 29.5” | 10 | 27.5” | 6 | 27.5” | 6 | 20.5” | 4 | 15” | 4 | 25.5” | 2 | 27.5” | 2 | N/A | N/A |
| 3814 | 39.5” | 8 | 38” | 2 | 25” | 2 | 9” | 4 | N/A | N/A | 20” | 2 | 22” | 2 | N/A | N/A |
| 3825 | 39.5” | 10 | 38” | 4 | 30.5” | 4 | 15” | 4 | N/A | N/A | 25.5” | 2 | 27.5” | 2 | N/A | N/A |
| 3835 | 39.5” | 10 | 38” | 6 | 30.5” | 6 | 20.5” | 4 | N/A | N/A | 25.5” | 2 | 27.5” | 2 | N/A | N/A |
| 3845 | 39.5” | 10 | 38” | 8 | 30.5” | 8 | 26” | 4 | N/A | N/A | 25.5” | 2 | 27.5” | 2 | N/A | N/A |
| 5223A | 53.5” | 6 | 52” | 4 | 19.5” | 4 | 15” | 8 | 9” | 4 | 15” | 3 | 16.5” | 4 | 14.25” | 2 |
| 5225 | 53.5” | 10 | 52” | 4 | 30.5” | 4 | 15” | 6 | 9” | 4 | 25.5” | 3 | 27.5” | 3 | N/A | N/A |
| 5225A | 53.5” | 10 | 52” | 4 | 30.5” | 4 | 15” | 8 | 9” | 4 | 25.5” | 3 | 27.5” | 4 | 14.5” | 2 |
| 5235 | 53.5” | 10 | 52” | 6 | 30.5” | 6 | 20.5” | 6 | 15” | 4 | 25.5” | 3 | 27.5” | 3 | N/A | N/A |
| 5245 | 53.5” | 10 | 52” | 8 | 30.5” | 8 | 26” | 6 | 20.5” | 4 | 25.5” | 3 | 27.5” | 3 | N/A | N/A |
| 5255 | 53.5” | 10 | 52” | 10 | 30.5” | 10 | 31.5” | 6 | 26” | 4 | 25.5” | 3 | 27.5” | 3 | N/A | N/A |
| 6025 | 62” | 10 | 60” | 4 | 30.5” | 4 | 15” | 6 | 9” | 4 | 25.5” | 3 | 27.5” | 3 | N/A | N/A |
| 6035 | 62” | 10 | 60” | 6 | 30.5” | 6 | 20.5” | 6 | 15” | 4 | 25.5” | 3 | 27.5” | 3 | N/A | N/A |
| 6036 | 62” | 12 | 60” | 6 | 36.5” | 6 | 20.5” | 6 | 15” | 4 | 31.5” | 3 | 33.5” | 3 | N/A | N/A |
| 6046 | 62” | 12 | 60” | 8 | 36.5” | 8 | 26” | 6 | 20.5” | 4 | 31.5” | 3 | 33.5” | 3 | N/A | N/A |
| 6046A | 62” | 12 | 60” | 8 | 36.5” | 8 | 26” | 8 | 20.5” | 4 | 31.5” | 3 | 33.5” | 4 | 17.75” | 2 |
| 6056 | 62” | 12 | 60” | 10 | 36.5” | 10 | 31.5” | 6 | 26” | 4 | 31.5” | 3 | 33.5” | 3 | N/A | N/A |
| 7225 | 72” | 10 | 70” | 4 | 30.5” | 4 | 15” | 6 | 9” | 4 | 25.5” | 3 | 27.5” | 3 | NA | NA |
| 7226 | 72” | 12 | 70” | 4 | 36.5” | 4 | 15” | 6 | 9” | 4 | 31.5” | 3 | 33.5” | 3 | N/A | N/A |
| 7236 | 72” | 12 | 70” | 6 | 36.5” | 6 | 20.5” | 6 | 15” | 4 | 31.5” | 3 | 33.5” | 3 | NA | NA |
| 7246 | 72” | 12 | 70” | 8 | 36.5” | 8 | 26” | 6 | 20.5” | 4 | 31.5” | 3 | 33.5” | 3 | N/A | N/A |
| 7256 | 72” | 12 | 70” | 10 | 36.5” | 10 | 31.5” | 6 | 26” | 4 | 31.5” | 3 | 33.5” | 3 | NA | NA |
| 7276 | 72” | 12 | 70” | 14 | 36.5” | 14 | 42” | 6 | 36” | 4 | 31.5” | 3 | 33.5” | 3 | N/A | N/A |
| 7276A | 72” | 12 | 70” | 14 | 36.5” | 14 | 42” | 8 | 36” | 8 | 31.5” | 4 | 33.5” | 4 | NA | NA |

| Pallet # | Description | 4” x 4” Length | Qty. per Pallet | 2” x 4” length | Qty. per Pallet | 1” x 6” length | Qty. per Pallet |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2638P | Small harrow pallet |
|  | 25.5” | 3 | 38.0” | 6 |
| 3848P | Harrow mount arm pallet |

38.0”

48.0”

5

| 6 |
| --- |
| 4848P | Tire pallet |
|  | 48.0” | 3 | 48.0” | 8 |
| 6038P1 | Granular tank top pallet |

38.0”

57.0”

2

| 4 |
| --- |
| 6038P2 | Granular tank bottom pallet | 38.0” | 3 | 60.0” | 8 |
| 8874 | Heavy harrow pallet | 88.0” | 2 | 74.0” | 4 |