DEPTH MICROMETER

## Calibration procedure #7

Environment:

Environment must be relatively dust free.

Clean inspection tools and surrounding area with citri-clean and lint-free wipes.

# A.	VISUAL INSPECTION

- Inspect bottom of measuring instrument surface, which could affect proper calibration.

- Inspect anvil for wear, nicks, or burrs.

- Check for proper instrument function’s:

Spindle locks, thimble ratchet.

- Inspect readability of sleeve, and thimble numbers and lines.

# B.	CALIBRATION

- Clean granite surface with lint free cloth or wipes.

- Clean bottom of measuring instrument and gauge blocks. Used in calibration.

- Place instrument on granite surface. Check reading if instrument does not read .0000 adjust sleeve.

- Measure depth at .250, .500, .750, 1.000 at depths greater than 1.000” use proper length gauge blocks.

- Measure by placing same size gauge blocks on opposite sides of micrometer.

- Record actual measurements on inspection report.