PIVOT HOUSING PRESS PROCEDURE

SAFETY

You must wear a full face shield when pressing the bushings.

Caution:  The nylon bushings can shatter if something catches or they are not completely lined-up.

Keep all body parts well away from any point where it might get pinched.

Stand as far back as possible when pressing in bushings.

CHECKS

Before plugging in, check the 600 volt cable for damage to the outer rubber covering and the plug-in end for any cracks or chips, etc.  If any unsafe condition exists, let your supervisor know immediately after locking-out the power supply.

Check the hydraulic lines and connections for leaks or damage before you turn on the hydraulic unit.

Make all hydraulic line connections before power supply is turned on.  Never make any hydraulic connections when the lines are under pressure.  To release pressure in hydraulic lines; with the hydraulic unit turned “off” work the cylinder lever back and forth a few times.

Power supply breaker must be turned “off” when connecting the 600 volt cable to the power supply.

Make sure to clean the ends of the hydraulic lines before you plug them in.

Turn on power supply breaker and the hydraulic unit and move the empty cylinder rod “in” and “out,” to make sure everything is working normally.

OPERATING PROCEDURES

With the cylinder rod fully extended, slide on the correct size die, nylon bushing, pivot housing, nylon bushing, correct size die and the cylinder end clamp, in that order.

Make sure cylinder rod end clamp is correctly seated in the cylinder rod groove before starting to retract the cylinder.

Make sure that nothing will catch on the housing support when the cylinder is retracted.

Hold the top of the pivot housing, making sure everything is lined up, and then slowly pull the cylinder in.

Caution:  The bushing must be lined up with the pivot housing or it will crack, break or shatter causing possible injury.

Note:  On the DR-651W you need to put a spacer between the cylinder and the first “die” to get the bushings placed in the correct position inside the pivot housing.

Make sure that the “dies” are right up against the pivot housing on both ends before extending the cylinder rod.  Fully extend the cylinder rod, remove the clamp and slide off the pivot housing and remove the dies.

Always turn “Off” the hydraulic unit when not using the press.  Turn off the main power breaker when leaving the area or at the end of the shift.

Clean up your work station and area after use or before shift change.