SPRING COMPRESSOR (SDX) PROCEDURE

## SAFETY

- The safety guard must be in place and working properly. (Must move down over spring when spring is being compressed).

- Keep hands and all other body parts away from the compression area when spring is being compressed.

## CHECKS

- Visually check the spring compressor for any damaged, loose or missing parts

before use.

2.   Do a “dry run” without the spring and it’s components to see if the compressor

operates smoothly and that the guard moved down over compression area,		and back up as required.

3.   Check the operation of the “IN – OUT” lever and the two (2) green “Start”

buttons to make sure that they operate properly.  The compressor must only

start when both of the green “start” buttons are pressed at the same time.

## C.  OPERATION

1.   Make sure that the compressor cylinder is fully retracted and the guard up		before operation.

2.   Slide spring over tube and seat the cast collar over the end of the spring.

3.   Place the pivot tube of the main tube into its seat near the cylinder and with the

ears of the cast collar in its seat at the other end of the compression chamber.

Note:  Very important that both ends of the spring assembly are seated in		place before you start the compression cycle.

4.   With the “IN – OUT” lever in the “out position, (towards the spring compression

chamber), and making sure all body parts, clothing, tools, etc. are not in or		 near the chamber, press both of the green “start” buttons at the same time.		 The spring will	compress.

5.   Insert the bolt through the hole in the end of the spring tube and secure with a

locknut.  Note: Tighten the locknut until about 2 threads of the bolt can be		seen.

6.   Push the “IN – OUT” lever to the “IN” position, (away from the spring				compressor chamber), and again press both of the green “start” buttons at the	same time.  The cylinder will retract and the guard lifts.

7.   Remove the completed spring assembly.