SPRINKLER SYSTEM

RE-CHARGE PROCEDURE

- Turn alarms off when fire is extinguished.

- Close water supply valve to zone with fire.

- Open draining valve to zone.

- Replace blown heads with proper temperature heads.

- Close draining valve.

- Open water supply valve fill zone.

- Open water supply valve for pump. Turn on open zone valve and re-charge to 115-120 lbs. on top gauge. Re-charge will take 10-15 minutes.

- When re-charged shut pump off, close zone valve and water supply for pump.

- Put alarm back in service.