TANK PAINT LINE

COLOUR CHANGE PROCEDURE

Time guideline:	1 person  1 - 1 1/2 hours

2 people  1/2 - 1 hour

In order to avoid colour contamination the following process must be followed when changing any colour in the paint booth.

Equipment Required:

-	Air wand

-	Clean rags

-	Pail with clean lukewarm water

-	Wood or plastic cleaning instruments

-	Floor squeegees

-	Pressure washer with extra hose

-	Shovel

-	Floor mops and mop pail

-	Broom

-	Clean plastic bags

-	Tie wraps

-	Zambonie

-	Rain coat

-	Face shield

-	Neoprene gloves

-	Rubber boots

1.	Call (Company) Maintenance to come and disconnect guns and cables if necessary.

2.	Turn on:

a.	Booth exhaust

b.	Waterfall

c.	Make-up air

3.	Clean out and wipe off . . .

a.	Feed hoses and transfer pump hose.

-	With hose disconnected from hopper, bring hose into the booth and blow out hose from both ends.  DO NOT RESTRICT AIR IN THE HOSE!

b.	Remove from the booth and clean . . .

-	Magnets

-	Nozzles

-	Extensions, etc.

c.	Manual guns.

d.	Venturi pumps and wear sleeves

e.	Powder pick up tubes.

f.	Breathing air hose.

Remove all impact fusion as per TPL Booth/Ovens maintenance procedure.

4.	Clean out paint canisters

a.	Dump all of the powder out of canisters and seal it in a clean plastic bag.

b.	Clean all powder paint residual dust out from inside the canister.

c.	Remove the fluidizing plate from the hopper.  Using a blow gun, and blowing from the bottom side up, blow out the fluidizing plate.  DO NOT BLOW FROM THE TOP SIDE DOWN BECAUSE YOU WILL PLUG THE PORES IN THE PLATE!

d.	Put required color of powder into the canister.

5.	Clean up booth

a.	Remove all trash.

b.	Remove all floor dry or absorbent sock(s) from front of waterfall.

c.	Blow off floor

6.	Blow off (in the direction of the waterfall)

a.	Booth roof

b.	Track (including a thorough clean - out of all track - changers in the booth).  Switch the track changer back and forth to shake loose any debris, and then blow it out again.

c.	Booth walls

d.	Booth floor

Quality:	Ensure that everything is completely and thoroughly blown off.

7.	If colour is being changed due to:

a.	Changing colours on tanks, or

b.	Changing colours to paint a tank after doing large quantities of a different colour or a large structure

Then . . .

1.	The track and ceiling may need to be pressure washed.  Extra hose is kept at the titration table.  Connect together enough hose to reach the far north corner of the paint booth.  Operate pressure washer as normal.  Start at the oven doors and pressure wash working your way towards the waterfall.  DO NOT PRESSURE WASH DIRECTLY AT THE OVEN DOORS!

Note: The decision to pressure wash the paint booth may be left up to the Front Line Supervisor’s discretion.

2.	All water may be cleaned up using a zambonie.  The key for the zambonie is kept in the Security Office at the main entrance.  Contact security to obtain the key.  The zambonie is kept at the First Aid Room.

Note:	If you do not use the zambonie, use floor squeegee.  Push water towards waterfall and ‘shovel’ water into waterfall.

After pressure washing, blow the track, ceiling, track changers and lights dry using the long air wand.

8.	Clean all lights (including portable lights)

- use a clean wet (damp) rag.  Inspect and clean if necessary.

9.	Inspect (clean again if necessary) . . .

a.	Booth roof

b.	Track

c.	Booth walls, etc.

Remove all residual powder dust etc.

10.	Turn off waterfall.

11.	Mop floor if necessary.

12.	Contact (Company) Maintenance to reconnect guns and cables if they were disconnected.

13.	Return all powder equipment to proper storage areas in booth (including absorbent socks).

14.	Clean-up cleaning supplies.

15.	Perform Shift Start-up Maintenance Schedule.

16.	If zambonie was used, return it to the proper location and return the key to security.

COLOUR CHANGE CHECKLIST

|  | 1. Contact (Company) Maintenance to disconnect gun cables. |
| --- | --- |
|  | 2. Turn on booth make-up air, exhaust and waterfall. |
|  | 3. Clean hoses, guns, venturis and wear sleeve and breathing air hoses. 4. Clean powder pick up tubes. |
|  | 5. Clean canisters and refill with powder. |
|  | 6. Remove trash, floor dry, absorbent socks, and blow off floor. |
|  | 7. Blow off booth roof, track, walls and floor. |
|  | 8. Pressure wash booth roof, track, walls and floor. |
|  | 9. Clean up water on floor and blow dry the booth ceiling. |
|  | 10. Clean all lights. |
|  | 11. Inspect booth roof, track, walls, and floor. Clean again if necessary. |
|  | 12. Turn off waterfall. |
|  | 13. Mop floor. |
|  | 14. Contact (Company) Maintenance to reconnect guns and cables. |
|  | 15. Return all powder equipment to its proper location in the booth. |
|  | 16. Clean up all cleaning supplies. |
|  | 17. Perform Shift Start-up Maintenance Schedule. |
|  | 18. Return zambonie to its proper location. |
|  | 19. All necessary steps are completed and signed off. |