TILLAGE CLEVIS BENDER

A.  SAFETY

- Never operate unless you have received On The Job Training from a competent operator or Supervisor.

- Switch breaker box off before attempting to plug in 600 V plug.

- Be aware of the “pinch points” on the machine.

- Test the function of the bender prior to set up and operation.

- Do not attempt to disable the left hand safety lever.

# B.	OPERATION

- Ensure unit has received its Total Preventative Maintenance.

- Select, inspect and install proper radius of nose.

- Adjust bending limit switch stopper.

- Insert material making sure it seats properly on material supports.

- Bend part.

- Follow standard parts check procedure.

- Proceed with operation.