TRIP SPRING COMPRESSOR

SAFETY & OPERATING PROCEDURES

A.	INSPECTION

- Be sure to inspect spring compressor condition before and frequently during the shift and notify your supervisor of any needed repairs.

B.	OPERATION

- Place casting and housing pre-assembly into spring compressor making sure that it is placed properly between the two hold down blocks.

- Next, place proper spring over tension link, then be sure that the spacer flat is located properly in the correct spacer tube (right-hand side).

Note:  Be sure to stand far as far back as possible from the spring compressor cage.

- Then with one hand on the “SAFETY” Hyd. Lever and one on the operating lever, pull back, this action will compress the spring inside the casting and housing assembly.

- Be careful of any binding action, if binding occurs, stop and determine the problem (Do not force it).

- If no binding occurs assemble bolt and nut or nuts to the top of the tension link at the proper torque.

- Then with one hand on the “SAFETY” lever, push the operating lever to open the cage.

- Inspect the trip to see if the spring is positioned properly.  If it is not it will have to be repositioned.