SET-UP

AND OPERATING PROCEDURE

A. DAILY MAINTINANCE TO BE PERFORMED BEFORE START-UP

|  | Check Coolant level Check way lube lubrication tank level. |
| --- | --- |
|  | Wipe spindle taper with clean cloth rag and apply light oil |
|  | Clean chips from tool changer |
|  | Clean chips from way covers and bottom pan Check waste oil container at back of machine |

### B. START-UP PROCEDURES AND ALIGNMEMT

|  | If you are not trained and authorized to run this machine precede no further. Turn the machines main breaker on. |
| --- | --- |
|  | Turn on the main power located on the back of the VMC. |
|  | Turn on the machine, (Green Power on Button) |
|  | Wait for machine to start, Clear alarm messages |
|  | Press power up button to initialize machine and find machine home position. Machine will set X, Y, Z and A home positions Machine will select tool #1 |

C. MACHINE OPERATION

|  | Set all work coordinates and tool offsets before running programs |
| --- | --- |
|  | Ensure that work piece is clamped properly |
|  | Clean tool tapers before putting tools into carousel |
|  | If running in a lights out situation check that shop air will remain on or hook up local air compressor to VMC |
|  | Perform weekly, monthly, and bi-annual maintenance as required by maintenance schedule |

D. SHUTDOWN PROCEDURES

|  | Clean the machine out and wipe the surfaces off. (Interior & exterior). Ensure area around machine is clear and spilled coolant is absorbed. Remove all fixtures if job is finished. Clean any tools and holders removed from machine and stored back into racks |
| --- | --- |
|  | Make sure the conveyor is shut off and the door is closed. |
|  | Push the emergency stop button or power down button. Wait while the machine saves the data until the screen goes dark, before shutting off the main power. |