BARRING AND STRAPPING PROCEDURE

FOR SOUTH PAINT LINE

Warning:	Failure to understand and follow these procedures may result in severe equipment damage and track downtime.

1.	Any item which is loaded on the paint track which has the potential to swing or fall when running through the pre-treatment system must be secured to prevent swinging or falling to prevent damage to equipment and track downtime.

2.	Items which are 36" long and over and which are hung vertically on the paint track must be secured in place by using two (2) 32" long hooks on each end of the rack, with one hook facing the inside of the track and the other the outside of the track.

3.	Place one (1) 3/4" dia. bar of appropriate length on each side of the items to be secured and hanging in the 32" long hooks used in step #2.

4.	Use bungee cords to strap the two bars together.  Place one near each end of the bars and one in the center.

Note:	If the bars have to potential to slip off the hooks, use wire ties to secure in place.

5.	For items which are between 18" and 36" long follow steps #2 - #4 but using a 16" long hook instead of the 32"

6.	On items which may fall off the line from the force in the pre-treatment system, use a wire tie to secure in place if the items cannot be hung on small bars in R10, (universal racks), or barred in steps #2 - #5.

7.	If parts which are hung on paint track form a natural pathway for one (1) 3/4" dia. bar to connect each part together as through a series of holes etc., where each part will be unable to come off the bar, you can use only (1) bar which is then tied to each end piece.

8.	Items which are hung in R10 universal racks on hooks and have the potential of falling must be strapped down with a bungee cord or tied with wire ties.

9.	Remove all bars, straps, ties etc., after the items are through the pre-treatment system and before the paint booth.