COMPACTOR SAFETY & OPERATING PROCEDURES

TRI-PAK ENVIRONMENTAL SYSTEMS

A.	SAFETY

- Under no circumstances should people climb into the charge chamber (hopper) of the compactor without first locking out the main power disconnect switch.  “Use Plant Lockout Procedures”

- Do not place any liquids or containers of liquid into the compactor.

- Do not dispose of anything that could be considered a hazardous waste, such as:  paint, oils, liquid, flammable solids, etc.

- When operating the compactor stand away or to the side of the charge chamber (hopper) just in case something flies out under impact.

- When climbing on the upper deck be sure of your footing.

B.	OPERATING INSTRUCTIONS

- To start machine:

- Load rubbish or garbage into charge chamber (hopper) of compactor.

- Turn control panel keyed selector switch to “on”.

- Press “start” button.  Machine will cycle automatically and stop at rear.

Note:  machine is set to cycle two times.

- Red jam full light:  The red light when lit is telling you that the container is full.  Should you encounter this, place “Hopper Full” sign on compactor and contact the Safety Department Manager.

- To stop compactor:

- In case of emergency press the red emergency stop button.  This will immediately stop the compactor even in mid cycle.  Switching the key to “STOP” or “OFF” during cycle will not deactivate the cycle.

- Press “STOP JAM FULL” button located on south side control panel.