IRONWORKER

SAFETY & OPERATING PROCEDURES

A.   SAFETY:

- Your foot must be completely removed from the pedal box after completing each cut, on machines, which are not equipped light curtains or other safe guards.

- Use proper shutdown procedures when changing punches, dies, blades, or shims.  Shut off the main power and have the key, (switch) in off position when changing punches and dies.

- Make sure all guards are in place and that all table adjustment bolts are tight.

- Don't ever try to grab a piece as it is being cut.  Remove small pieces from the blade area with a hook, never your fingers.

- Don't run the shear on 'automatic' unless you are properly trained by your FLS or area designate.

- Turn the main power off when leaving the machine unattended.

- Never put your hands near a Hazardous area or Pinch Point, if a part is too large to sit on the ironworker table without your assistance, only hold the part if your hands are completely off the ironworker table and no body part could be susceptible to injury.

B.	OPERATION:

1.      	a.  After changing punches, dies, blades or shims, lower the punch/ shear by hand  (or jog) to check the clearance and alignment.

Note:  Most Ironworker Manufacturers recommend Punch and Die alignment is checked before each set-up and periodically throughout longer runs.

b.  Before installing a Punch or a Die into the Ironworker, they must be slipped checked Failure to do so could cause tooling damage and/ or personal injury.

- Always adjust material hold-downs to allow material to just slide under before attempting to shear. Don't allow more than 1/8" clearance between the material and the hold-down clamp. Check to confirm proper blade clearance (use feeler gauges).

- Never put material in from the back-side of the shear.  Always cut from the roller table side making sure the material is under the hold-down.

- Don't attempt to shear off a piece of material shorter than its thickness.

- Don't cut pieces that have less than ½" under the hold-down.

- a.   Use proper size stripper insert or plate.

- Punch depth must be set to avoid stripper damage.

- Make sure stripper is fully engaged and tightened before operation.

- Do not attempt to punch material thicker than the diameter of the punch.

- Always put your tools back after you set up.  Practice good housekeeping at all times.