LIQUID PAINT MIXING

APPLICATION PROCEDURE

Prior to spraying Urethane paint, the following mixing must be done:

Put paint barrel on - line with small mixer.

Turn mixer on and increase the mixing speed slowly until the paint around the edges of the barrel is beginning to move in a circular fashion.

Maintain that mixing speed until:

All the paint is flowing free enough to rapidly circulate.

Paint has a smooth consistent appearance.

Note: If air bubbles begin to form in the paint - the mixer is set too high  ( lower the speed and allow it to mix longer.

Turn the mixer down to a level that will maintain a smooth consistent appearance (even around the edges) during pumping.

Paint is now ready to spray.