MILLING MACHINE

- SAFETY

  - Never put hands near a rotating cutter.

  - Be aware of sharp edges on the cutting tool and work piece.

  - When cutting direct chips away from you (be aware of other operators in the area).

  - Make sure all components are secure before cutting.  This includes:

    - Tooling inserts

    - Draw bars

    - Work piece and fixture

  - Disengage crank handles after use (failure to do this can cause the handle to spin very fast when rapid traversing).

  - Never rapid traverse table to end of stroke, this will jam the lead screw.

  - Practice good housekeeping at all times.

  - Remove vice handle.  Prevents jamming on ways.

- OPERATION

  - Inspect the condition of the cutting tool before use including:

    - Cutting edges

    - Insert pockets

    - Threads - clamping and draw bar

    - All contact areas - tapers, threads, etc.

  - Inspect the condition of the work holding device.

    - All fastening hardware - clean or replace if necessary.

    - Clean mounting surfaces - mill table, base of vise, fixture, etc.

  - Make sure speeds (SFPM) feeds and depths of cut are set according to the tooling, work piece and job requirements. Note: Be sure to dial the head in on the mill at regular intervals, especially after a crash!

  - Where required make sure adequate type and amount of coolant is applied.

  - Make sure when you are ready for operation all table locks, locking mechanisms for over arm hardware is secured, draw bar.

Free table locks before operating feeds (servos).

  - Clearance - make sure there is adequate clearance where required.

  - Treat mill fixtures, tooling and milling machines with respect.

  - If unsure of how to do something - ASK!

  - Use table stops as required.

  - Debur all sharp edges on work piece.

  - Listen to your machine for changes in sound during operation - changes could indicate:

    - Worn or damaged tooling

    - Loose setup

    - Loose machine components

    - Improper direction of travel

  - Be aware of Climb milling vs. Conventional milling.

- AFTER OPERATION

  - Clean all components on mill and wipe off all tooling fixture, fastening devices, etc.

  - Before putting things away:

    - Inspect the condition of the fixture

    - Inspect the condition of the tooling - worn inserts, burrs on mounting surfaces, etc.

    - Inspect all hardware for wear, damage, etc.

The above step will make your next setup easier if you get in the habit of taking care of your machine tooling, etc.