# Minster Press #22048

### Start Up Procedure (only) *Not Operating

A.	START-UP

## Turn on main disconnect for press and hyd. Unit. “Ground Connected”  And “Flywheel Stopped” lights should be on. If not check that disconnects on hyd. panel and press panels are on.

## Push master start push button. Green light should come on.

## Adjustments to slide height can be made at this time.

## Push lube motor start push button. Green “Lube Motor On” light and red “Lube Fault” light should come on.

## Push “Lube Reset” push button for 8 seconds and release. “Lube Normal” light should come on. If not, repeat. It may take several times at start of shift.

## Push “Hydraulic Pump Start” push button for 5 seconds. Green light should come on and stay lit when button is released. If light does not stay on, hold button for longer duration.

- Push and hold “Main Motor Start”. Push button until “Main Motor Running Fwd” and “Flywheel in Motion” lights are on.

- Wait 10 seconds for flywheel motor to come to full speed before cycling press.

*Proceed with normal punch press operation according to applicable procedures at this time.

#### B.	SHUT DOWN PROCEDURE

- Push “Auto Shut Down” push button.

- Shut off main disc for press and hyd. unit only after “Master Start” green light has shut off.

* Important - Do not use emergency stop push button for normal shut down of press.

* “Main Motor Stop” push button can be used when setting up.