#34 MULTI-SPINDLE DRILL

ROBOTICS 550 TRIP CELL

SAFETY AND OPERATING PROCEDURES

SAFETY:

Know where the emergency stop buttons are located on your machine before operating.

Only use a chip hook or brush to remove drill chips.  Never reach between turning drill bits and never attempt to grab drill chips by hand.  Wear gloves when possible and handle all materials carefully.  Be cautious of sharp burrs.

Do not operate the drill wearing loose clothing, finger rings, or jewelry.  Long hair must be tied up or tucked under the hard-hat.

OPERATION:

Do a dry run without a piece after set up to ensure proper settings have been done prior to running the job.

Ensure the drill jig is clamped properly.

Ensure material clamps are functioning properly and aligned before beginning production of parts.

Ensure reamers are adjusted to the proper length.  Reamers should be inspected regularly.  At least every 30 cycles.

Ensure reamers and bushings receive an adequate flow of coolant.

Keep the work area as dry and free of chips as possible.

Be careful when handling the part, before and after drilling to ensure excellence in quality.  Check parts regularly to ensure parts are to specs.

Do not use the drill jig as a way of banging the chips off a part.  The multi-spindle drill is set up to produce an excellent overall quality part while maximize efficiency and reliability.  Do to the complexity of the machine and set up, we ask that you do not make any adjustments.  If you feel that something is not performing as it should or suspect a problem.  Lockout the drill (using proper lockout procedures) and contact your immediate supervisor.

Practice good housekeeping at all times.