MAINTENANCE CHECKSHEET

WARNING:  Auto Guns must be turned off and locked out prior to any clean-up or maintenance done to or around Auto Guns (including squeegee around guns).

DAILY SYSTEM START UP INSPECTION:

- Check and Inspect the Following:

  - Gun grounding connections (all 20).

  - Booth grounding connections (all 9).

  - Copper ground bar touching flat bars on the line.

  - Drive Air regulators for booth on/off line switch (50-90 PSI) - 2 regulators

  - Check Air Dryer

    - Unit must be on at all times.  (If it is off, call Paint Line Maintenance.)

    - Temperature at -40F (May vary, if so, monitor and report.)

    - Air pressure at or greater then 100 PSI

  - Booth position (ensure that it is on line).

  - Powder collector and hopper (alignment & latching).

  - Clear platforms and booth interior of all obstructions.

  - Final filters.  (Check from front for powder leakage)

  - All powder delivery air lines (look for any kinking, binding, tearing or obstructions).

  - Check oil level in oilers. (2)

  - Pump mounts, venturi pump, hoses and gun connections. (All connections are to be tightened.)

  - All gun nozzles (aim as required).

  - Connections on all pattern and ionization air lines to auto guns.

  - UV detector system (clean and test).

  - Photo sensors for gun triggering system (alignment and sensitivity)

  - Auto guns (alignment and even spacing).

  - UV head air supply (15 PSI).

Note:	If booth cannot be kept within specifications contact Maintenance.

- Turn the Booth on and record the Booth Hours.  Then, perform the following:

  - Test the final filter alarm.

  - Check the booth lights (if burnt out contact Electrical Maintenance for replacement).

  - Test low level powder alarm.

  - Ensure that the following are within operating parameters:

    - Gun array pressure (50 PSI)  - 2 gauges

    - Final filter pressure (0.5 - 1.5 inches of water)

    - Purge pressure (80 - 85 PSI)

    - Purge delay (10 - 15 sec.)

    - Fluidization pressure (4 - 8 PSI)

    - Screener pressure (Charcoal 20 PSI)

    - Master control module pressure (90 - 100 PSI)

    - Collector pressure (2.0 - 5.5 inches of water)

  - Log gauge reading for collectors and hoppers.

  - Check powder level & condition in collector and hopper.

    - Proper fluidizing

- Turn computer processor on.

- Turn Auto Guns on and Inspect:

  - Rack grounding with Fluke Multimeter.  (This is to be done when first rack is entering the booth.)

  - Regulator pressure settings on all guns.

  - Adequate spray pattern

    - adjust the powder, fluidization pressure & KV’s

  - Auto Gun tip ionization air setting.

    - adjustment is done by “feel” and expertise

    - too low - results in powder build-up on electrode.

    - too high - disturbs the spray pattern.

  - Test and record air flow in booth and booth openings.  See Wagner Powder Booth TPM Procedure.

    - Ensure booth is on line.

    - Adjust air flow damper to get CFM reading between 100 - 125 (Max-150)

- Perform K.V. Testing on auto guns; record on sheet, and in log book.

- Turn Auto Guns off.

- Turn Manual Guns on.

  - Set manual gun pressures & KV’s

  - Perform K.V. Tests on manual guns.  (To be done every shift.)

- Turn Manual Guns off.

HOURLY INSPECTION:

WARNING:  Auto Guns must be turned off and locked out prior per lock-out procedure to any clean-up or maintenance done to or around Auto Guns (including squeegee around guns).

- Check the following areas and adjust as necessary:

  - Powder hopper

    - proper fluidization

    - foreign objects (clean as necessary)

  - All gun spray patterns

    - clean nozzles as necessary.

  - Pump venturi (build - up & plugging)

  - Powder squeegee from booth floor into hopper.

END OF POWDER RUN INSPECTION:

To be done at the end of every run of parts (as times permits) - up to three times per shift.

- Booth Clean-up increase booth air to ensure powder collection during clean-up.

- Clean the following:

  - Pump venturies (build-up & wear)

  - Blow-out powder hoses.

    - always blow from the pumps toward the auto guns

  - Squeegee powder from the booth floor into the collector.

  - Squeegee interior of booth and vestibules.

  - Blow off powder guns into the booth in order to reclaim the powder.

  - Clean powder path in all guns and replace worn or damaged parts.

    - including gun nozzles and tips

  - Clean the outside of the booth.  (Floors, etc.)

- Return booth air to normal operating levels.

WEEKLY INSPECTION:

- Friday

  - Inspect cartridge filters for:

    - Powder build-up

    - Leaks

  - Inspect final filters for:

    - Powder build-up

    - Leaks

Note: Report any leaking filters to supervisor immediately

.

  - Inspect vibratory screener for proper operation, cleanliness and vacuum.

  - Inspect glass exhaust bowls. Report any dirt, powder or other residue found in bowls to supervisor immediately.

  - Align pulse valves. Report any loose or valves leaking air to supervisor immediately.

  - Fill oilers/empty oil trays.

  - Perform ionization air test.

# (Company) POWDER BOOTH

SHIFT MAINTENANCE CHECK SHEET

Date:                                                        		Employee #:

START-UP CHECK LIST (Initial or enter appropriate data):

Gun ground connections (20)                    			Oil level in oilers (2)

Booth ground connections (9)                   			All connections: Mounts

Ground bar touching flat bars                    				             Venturi

Air Dryer: On             Temp.             PSI            /          /          		             Air Lines

Align Photo sensors		          			All gun nozzles

Auto gun alignment		          			Auto gun air line connections

Powder collector alignment	          			UV head PSI

Clear Platforms/Booth Interior

Final Filters

Powder Delivery Hoses

Booth lights

WITH THE BOOTH ON . . . 		Booth Hours:

Drive Air regulators PSI (2)           	  /          	                                           Test UV detector system

Final filter alarm		              					Purge delay (sec.)

Low level powder alarm        _____		                    	Fluidization PSI (4 gauges)

______/_____/_____/______

Gun array PSI’s (2)	               /            				Screener PSI

Final filter Pressure (WC)	             	 				Master control module PSI

Purge pressure PSI	            	 				Collector Pressure (WC)

Powder condition/level.	    _____

Rack ground check (with Fluke Multimeter)

AIR FLOW:

Entrance top  		Bottom  		Exit top  		Bottom

South Man Station				North Man Station ______

South Vestibule 				North Vestbule  _______

Centre of Booth

Note:	When performing these air flow tests ensure you are not standing in front of the opening you are measuring as this will effect the 	reading.

K.V. TESTS

Outputs	1  		6  		11  		15

2  		7  		12  		16

3  		8  		13  		17

4  		9  		14  		18

5  		10

EVERY SHIFT

Manual	North

South

(Company) POWDER BOOTH

# WEEKLY MAINTENANCE CHECK SHEET

DATE: ____________________                                 TIME:  __________________

SHIFT: ___________________                      BOOTH HRS:  __________________

DARK GREY           RED                EMP #

GLASS EXHAUST BOWLS  (2)       _____                  _____               ________

VIBRATORY SCREENERS              _____                  _____               ________

CARTRIDGE FILTERS                     _____                  _____                ________

ALIGN PULSE VALVES                  _____                  _____                ________

FINAL FILTERS                                _____                  _____                ________

EMPTY OIL TRAYS  (3)                  _____                   _____                ________

FILL OILERS (2)                               _____                   _____                ________

VENTURI WEAR SLEEVE INSPECTION

- must be measured with a digital venire calipers

- inside diameter opening must not be greater than .2400” or it must be replaced

- must not be any grooves, gouges, damage, etc. or it must be replaced

- average inside diameter opening of new is .2300”

DARK GREY VENTURIS      EMP #: __________         RED VENTURIS                     EMP #: __________