PAINTERS SHIFT CHECKLIST

(Initial in box when complete)

Date:  							Shift: 			Days:  (	Evenings:

Person

| Responsible |
| --- |
| Complete |
| Skim detect from waterfalls. |
|  | Flush out guns (also to be done if line is down longer than 5 minutes) |
|  | Clean gun filters, tips, air caps, gun nose, outside gun threads; check guns over for safety. Quality: Ensure tips and air caps are completely clean before placing back on guns. |

Person

| Responsible |
| --- |
| Complete |
| Skim detect from waterfalls. |
|  | Flush out guns (also to be done if line is down longer than 5 minutes). |
|  | Sweep off front man lifts in both booths. |
|  | Check, clean and align nozzles in 3 Stage Wash. |

| First Stage | Plugged |
| --- | --- |
|  | Cleaned |
|  | Worn out |
|  | Changed |
| Second Stage | Plugged |
|  | Cleaned |
|  | Worn out |
|  | Changed |
| Third Stage | Plugged |
|  | Cleaned |
|  | Worn out |
|  | Changed |
| Quality: Nozzles #8060 go in Stage One and #6540 go in stages two and three. |

Person

Responsible

Complete

Inspect Dry-Off Oven, Bake Oven, and Wash for parts which may have fallen off and/or other safety/quality concerns.

Rotate and align wear parts in blast machine.

| Note: Parts that fall off prior to wash pretreatment must be rehung to be pretreated properly. |
| --- |
|  | Back up line; blow and tack off parts. |

Person

| Responsible |
| --- |
| Complete |
| Flush out guns (also to be done if line is down longer than 5 minutes) |
|  | Pick up plastic bags, plugs, and caps from booth floor. |
|  | Skim detect from waterfalls. |
|  | Change dirty light bags. |
|  | Change dirty gun covers. |
|  | Check and clean (if necessary) filter screens in waterfalls. |

Two painters are to go for coffee 5 minutes before the horn and come back 5 minutes before the second horn.  They are to:

flush in all 4 paint guns.

put tips/air caps on.

start up the blast machine.

start the ovens (dry-off and bake ovens).

start the man lift pump.

start the breathing air compressor.

start the front waterfall (back painters turn on back waterfall).

get ready to paint.  (Put tips, etc. on front guns.)

at the horn, start the track, and the 3 Stage Wash

Once per shift, check and record the following:

| 1.)Check/clean pump filter screens: |
| --- |
| 2.)Check/clean wash tank level probes: |
|  | Stage One: Checked: |
| Stage One: Checked: |
|  | Cleaned: |
| Cleaned: |
|  | Stage Two: Checked: |
| Stage Two: Checked: |
|  | Cleaned: |
| Cleaned: |
|  | Stage Three: Checked |
| Stage Three: Checked: |
|  | Cleaned: |
| Cleaned: |