PANTHER PORTABLE ELECTRIC

PRESSURE WASHER

SAFETY & OPERATING PROCEDURE

A.	START-UP

If using an extension cord on 110 volt on 220 volt machines.  Be sure it is a sufficient gauge size.

Make sure pump has proper oil supply by checking dipstick or sight glass at the side of the pump.  Oil level should be at the center of glass at the red dot.

a)  when attaching your garden or input hose to the inlet fitting at the pump.  Make sure all connections are secure.

b)  Check to make sure screen is free of debris.

Attach quick coupler of hose assembly to female coupler at pump.

Turn on water supply.

B.	OPERATION

Squeeze trigger gun on to provide water flow and start motor.

The maximum pressure of the unit will already be set.  To reduce pressure turn red knob on top of unloaded valve counter clockwise.

Do not let pump run in bypass mode (motor running, trigger off) for longer than 5 minutes.  Pump seals may be damaged by heat.

Maximum water inlet temperature is 140oF.

To apply chemical, insert the clear chemical suction tube and strainer into the soap pail.  By using the dual nozzle or twin lance reduce the spray pressure.  This pressure drop will activate the pump injector and draw chemical into the hose.  Adjust chemical flow at the red knob on the front of the pump.

To quit chemical draw and rinse.  Turn nozzle holder on twin lance until pressure returns to its normal high setting.  It is not necessary to turn chemical flow valve off.

Be sure to change pump oil at least once a year.

Do not allow unit to freeze.

C.	SAFETY

Caution: For your own personal safety it is critical that the Panther Pressure Washer is only used with a ground fault plug. Failure to insure that this is done can result in a fatality due to electrocution.

Make sure you wear your personal protective equipment.

Optional:

Face shield or safety goggles.

Waterproof coat or apron.

Waterproof steel toed boots.

Never point the direction of spray at a person (high pressure spray can pierce skin).

Never spray in the direction of people where dirt or stone fragments could be propelled at people causing injury.