PNEUMATIC DIE GRINDER

A.	SAFETY

When operating the grinder always wear a full face shield, which provides you with clear visibility, and gloves.

Handle the grinder with care to prevent damage and reduce the possible risk of injury.

B.	INSPECTION

Visually inspect the grinder before connecting to the air supply to ensure the following:

The body of the tool must not be cracked.

The chuck and chuck nut must not be cracked or otherwise damaged.

The safety latch is in place and operating correctly.

Ensure that the RPM rating of your accessory is rated at or higher than the RPM rating of the tool.

Make sure that the accessories are firmly tightened into the chuck of the tool so that there is no danger of an accessory coming loose and flying off during operation of the tool.  Do not over tighten as the chuck nut may crack.

C.	OPERATION

Clamp smaller pieces to be ground in a vise.

The grinding accessory must come to a complete stop before leaving the grinder to inspect your work.

Unplug the air supply from the die grinder before you attach or remove any accessories.

Report any unusual vibrations, rattles, or odors to your supervisor immediately.