PAINT BOOTHS

POWDER OUTPUT TEST PROCEDURE

- Ensure powder is fluidizing properly and there are no obstructions in the powder paths of all guns, hoses and venturi pumps.

- Auto guns:

  - Turn auto guns to “Manual” mode.

  - Turn each auto gun power supply off.

  - Turn each auto gun on one at a time and:

    - set K.V.’s to zero.

    - set flow rate air to normal operating psi.

    - set atomizing air to normal operating psi.

  - Turn auto gun power off when adjustments are complete.

  - Disconnect the powder hose from the gun.

  - Insert the powder hose into the powder containment unit.

  - Ensure that the openings around the vent hose and around the powder hose are secured to prevent powder leakage.

  - Turn on the appropriate power supply for 60 seconds.

- Manual guns:

  - Turn controller power on.

  - Pull gun trigger and:

    - set K.V.’s to zero.

    - set flow rate air to normal operating psi.

    - set atomizing air to normal operating psi.

  - Release trigger.

  - Disconnect the powder hose from the gun.

  - Insert the powder hose into the powder containment unit.

  - Ensure that the openings around the vent hose and around the powder hose are secured to prevent powder leakage. Be careful not to restrict powder entering the powder containment unit.

  - Pull the gun trigger and hold for 60 seconds.

- Remove the powder hose from the unit.

- Weigh each unit separately.

6.    Record all gun settings and powder weights for each gun.