TANK PAINT LINE

TANK WASHING PROCEDURE

Attachments:	Tank Washing Checklist, Tank Paint Checklist

All Seeder Tanks (including Granular tanks) are to be washed using one of the following two processes:

1.	Automatic 3-Stage Cycle Wash - Cryscoat 347C, Rinse, Ultra Seal

- To be used for all Seeder tanks and all other normal washing.

2.	Individual Cycle Wash

- To be used only for specific situations.

A.	PERSONAL PROTECTIVE EQUIPMENT REQUIRED:

1.	Manual Wash Bay (when using Fleet line)

a.	Basic Plant requirements (hard hat, safety glasses, earplugs, and CSA steel-toe shoes).

b.	North Respirator face piece with fresh air line.

c.	Rain coat/suit

d.	Neoprene gloves

e.	Rubber boots

2.	Automatic Cabinet Wash

a.	Basic Plant requirements.

b.	Gloves etc. if booth requires entry or work when it is still wet inside.  Discretion is required.  DO NOT ENTER WASH WHILE THE SYSTEM IS RUNNING!

All Chemicals must be titrated and checked as per titration procedure and all chemicals must be within parameters.

A White Rag Test is required on the first tank washed every week, to be performed when tank comes out of the cabinet wash before it goes into the dry-off.

Do not allow the tank to dry down between any of the wash cycles or stages.

Note:	Prior to washing the first tank of the day, an automatic cycle must be run without a tank in the auto wash booth.  The purpose of this is to ensure the chemicals are thoroughly mixed.

B.	PROCEDURE

Inspect tank to be sure all prepping has been completed.

Hand sand all panels to remove any abrasive or debris with 180 grit sand paper.

a)	Check to ensure all high temperature silicone plugs are in place in the 1720, 2320, and 1330 tanks.

b)	Before placing tank in auto wash ensure basin level indicator light is out.  If light is on basin must be drained before pushing tank into wash bay.  May be drained manually or automatically using the proper key.

Bring tank into auto wash bay, being very careful to avoid spray pipes or nozzles.  Secure the hook to hold tank in place.

Quality:  Do not touch the blasted tank as any traces of dirt or grease will affect paint adhesion.

Lower the spinner nozzles.

Granular tanks - north spinner is lowered all the way into the middle of the tank.

- south spinner is lowered to within 8” - 10” of the top of the tank.

1720, 2320, 1330 tanks - spinner nozzles are lowered all the way into the middle of the tank.

* At this point, operator can select either a regular, automatic three -stage wash cycle wash or there is the option of choosing an individual cycle wash.  The individual cycle wash is only to be used in special cases when specifically requested, or in the event that the automatic three stage wash is not working properly.  Call Electrical Maintenance A.S.A.P if program is not working!

Automatic Three-Stage Cycle Wash

Turn selector switch to “3-Stage Auto”.

Press “start” button.  Tank will automatically be washed in the following sequence:

347C/Rinse/Ultra Seal

This cycle will automatically raise the spinner nozzles.

Manual/Individual Cycle Wash

Note:  In order to wash in manual/individual cycles you must contact Electrical Maintenance to run manual cycles.

Turn selector switch to “Manual”.

Press the “Manual Phosphate” button.  Tank will be washed with 347C solution.

When the “Phosphate” indicator light goes out (located on south side of control panel), press the “Manual Ultra Seal” button.  Tank will be washed with a rinse followed by Ultra Seal Solution.

When the “Ultra Seal” indicator light goes out, raise the spinner nozzles all the way to the top of the wash bay.  Make certain they are completely out of the tank.

* The rest of the procedure is the same regardless of which method you have used to wash the tank.

Open doors and take the tank out.  Ensure tank has even bluing.

Note:  Wait until basin has drained and spinner nozzles are completely out of tank before attempting to pull tank out of cabinet!

If tank is the first tank of the week, do a white rag test on a panel and record results on the Tank Pretreatment Record.

Push tank immediately into the dry-off oven and reset the burners.

Inform the painters of the tank in the dry-off oven.

Complete the checklist and Pretreatment Record and sign it off to the painters.  (Ensure you record any non-conformances on the Pretreatment Record.)

Complete you’re “After” set of titrations.

Close the doors and lower the spinner nozzles.

Turn the selector switch to “Manual”.

Press the “Manual Rinse” button.  A rinse cycle will run to clean the wash bay and rinse all lines out.

When the rinse is complete, the “Rinse” indicator light will go out.

Basin level indicator light will also go out.

TANK PAINT LINE

TANK WASH CHECKLIST

Date:

Wash Operator:

Tank I.D. #:

* Do not allow tank to dry down between cycles!

Emp. #:

|  | Inspect tank to ensure all prepping is complete. |
| --- | --- |
|  | Hand sand all panels to remove any abrasive or debris with 180 grit sand paper. |
|  | Ensure all wash solutions are in parameters. |
|  | Bring tank into wash cabinet. |
|  | Position tank in middle of booth and secure it in place (except granular tanks). |
|  | Lower spinner nozzles. |
|  | Select appropriate cycle and run cycle. |
|  | Raise spinner nozzles (if a manual cycle was run). |
|  | Pull tank out of the auto wash and inspect for even “bluing”. Perform white rag test if it is first tank of the week. |
|  | Push tank into dry-off oven, reset burners, and inform painters. |
|  | Complete your “After” set of titrations and complete all paperwork. |
|  | Run a manual rinse to clean auto wash cabinet. |

TANK PAINT LINE

PAINT CHECKLIST

Emp. #:

|  | Clean booth and track of any contamination. |
| --- | --- |
|  | When dry-off cycle is complete, pull tank out and place in painting position. |
|  | Allow tank to cool at least 15 minutes before painting. |
|  | Check tank for flash rusting, even bluing, and any non-conformances (repair if necessary and record as non-conformance). |
|  | Inspect tank hanger to ensure safe hanging of the tank. |
|  | Ground the tank. |
|  | Apply magnets. |
|  | Start waterfall. |

Paint tank in following sequence:

Hard to reach areas.

Interior of tank.

| Exterior of tank. |
| --- |
|  | Double check for missed panels/non-conformances. |
|  | Rotate tank upside down and push it into bake oven. Start cure cycle. |
|  | When cure cycle is complete, pull tank out and allow it to cool. |