WASH START UP PROCEDURE

Note:  Mondays or after a holiday or long weekend start wash burners 45 minutes to 1 hour earlier.  Wash should be started no later than 6:00 a.m. or 1 hour before shift begins.

- Make a quick inspection inside to make sure no one or nothing is inside.

- Check panel with entrance/exit/ tunnel fan indicating lights on it, to see that main disconnect is on and all indicating lights are on.

- Close disconnect switch on main control.

- Depress “Master Start” illuminate push/pull push-button switch.

  - “Master Start” light comes on.

  - Washer circuits are enabled.

- Pull “Washer Combo blower” illuminated push/pull push-button switch.

  - Combustion blower starts.

  - “Washer Combo Blower” light comes on.

  - Purge Timers start and “Purging” lights come on.

    - “Ignition Ready” lights come on when purge period is complete (about 2 minutes).

    - “Purging” lights go out.

Note:  The washer pumps may be started without the combustion blower being on.  However, the combustion blower must be on for the washer burner circuits to operate.

- Pull “Ignition Ready” illuminated push/pull push-button switches and hold until “Burner On” lights come on for that stage.

  - “Pilot On” lights come on when pilots are established.

  - “Ignition Ready” lights go out.

  - Timers reset.

  - Main burners come on.

    - “Burner On” lights come on.

    - “Pilot On” lights go out after release of “Ignition Ready” switches.

    - Burners modulate to maintain desired temperature.

    - If “Burner On” light for Main Burner goes out, wait until “Ignition Ready” light comes on and then repeat Step #2.

Note:  If or some reason any part of this cycle does not operate as it is supposed to contact Supervisor or Electrical Maintenance.